SECTION 08 52 00

WOOD WINDOWS

(ANDERSEN® ARCHITECTURAL SPECIALTY WINDOWS)

GENERAL

Specifier Note:  Data contained in this guide spec is accurate as of August 2007.  Due to ongoing product changes, this data may change over time.  Consult manufacturer for complete product details.

SUMMARY

Section Includes:

Wood Windows.

Specifier Note:  Article below should be restricted to statements describing design of performance requirements and functional (not dimensional) tolerances of a complete system.  Limit descriptions for composite and operational properties required to link components of a system together and to interface with other systems.

SYSTEM DESCRIPTION

Specifier Note:  Manufacturer recommends referring to website for most current product performance data.  Retain, edit, or delete language below to suit project requirements.  refer to www.andersenwindows.com for performance information.

Performance Requirements:  Provide products/systems that have been manufactured, fabricated, and installed to the following performance criteria:

Comply with 101/I.S.2/NAFS.

Performance Class:  <Specify performance class.>

Performance Grade:  <Specify performance grade.>

U-Factor (NFRC 100) :  <Specify U-Factor.>

Solar Heat Gain Coefficient (SHGC) (NFRC 200) :  <Specify SHGC.>

Outdoor-Indoor Transmission Class (OITC) (ASTM E90) :  <Specify OITC.>

Sound Transmission Class (STC) (ASTM E90) :  <Specify STC.>

Specifier Note:  Manufacturer recommends referring to website design pressure estimator for additional wind load information.  Retain, edit, or delete language below to suit project requirements

Structural Requirements: Provide products/systems capable of withstanding wind loads based on testing units representative of those indicated for Project that pass AAMA/NWWDA 101/I.S.2/NAFS, Uniform Structural Load Test:

Design Wind Loads: Determine design wind loads applicable to Product from basic wind speed indicated in miles per hour (meters per second) at 33 feet (10 meters) above grade, according to ASCE, Section 6, based upon mean roof heights indicated on Drawings.

Basic Wind Speed: <Specify wind speed.>

Importance Factor: <Specify importance factor.>

Exposure Category: <Specify exposure category.>

Wind Load Requirement: <Specify design pressure requirement.>

Specifier Note:  Article below includes submittal of relevant data to be furnished by Contractor before, during or after construction.  Coordinate this Article with Architect’s and Contractor’s duties and responsibilities in Conditions of the Contract and Division 01 Submittal Procedures Section.

SUBMITTALS

General:  Submit listed submittals in accordance with Conditions of the Contract and Division 01 Submittal Procedures Section.

Product Data:  Submit manufacturer’s product data and installation guides.

Shop Drawings:  Provide drawings indicating direction of operable parts, typical jamb, head and sill conditions, and special mullion reinforcement details.

Color Samples:  Submit selection and verification samples, including the following:

Cladding:  Submit color Samples of cladding.

Contract Closeout Submittals:  Submit the following:

Warranty documents specified herein.

Owner’s Manual:  Bound manual clearly identified with project name, location, and completion date. Identify type and size of units installed.  Provide recommendations for periodic inspections, care, and maintenance.  Identify common causes of damage with instructions for temporary repair.

Specifier Note:  Article below should include statements of prerequisites, standards, limitations and criteria that establish an overall level of quality for products and workmanship for this Section. Coordinate Article below with Division 01 Quality Assurance Section.

QUALITY ASSURANCE

Installer Qualifications:  Utilize an installer having demonstrated experience on projects of similar size and complexity.

Specifier Note:  Paragraph below should list obligations for compliance with specific code requirements particular to this section.  General statements to comply with a particular code are typically addressed in Conditions of the Contract and Division 01 Regulatory Requirements Sections.  Repetitive statements should be avoided.

Regulatory Requirements and Approvals:  <Specify applicable requirements of regulatory agencies.>

Certifications:

Insulating Glass Units:  Provide insulating glass units permanently marked with certification label of Insulating Glass Certification Council (IGCC) indicating compliance.

specifier note:  retain certification label requirements paragraph above or below.

Insulating Glass Units:  Provide insulating glass units permanently marked with certification label of Insulating Glass Manufacturers Association of Canada (IGMAC) indicating compliance with CAN/CGSB or ASTM E2190.

Specifier Note:  Retain paragraph below if preinstallation meeting is required.

Preinstallation Meetings:  <Specify requirements for preinstallation meeting.>

DELIVERY, STORAGE, and HANDLING

General:  Comply with Division 01 Product Requirements Section.

Comply with manufacturer’s ordering instructions and lead time requirements to avoid construction delays.

Delivery:  Deliver materials in manufacturer’s original unopened, undamaged containers with identification labels intact.

Storage and Protection:  Store materials protected from exposure to harmful environmental conditions and at temperature and humidity conditions recommended by the manufacturer.

Store materials and accessories off ground, under cover, and protected from weather and construction activities.

Specifier Note:  In Article below, state physical or environmental limitations or criteria for installation such as weather, temperature, humidity, ventilation or illumination required for proper installation or application.

PROJECT/SITE CONDITIONS

Field Measurements:  Verify actual dimensions of openings by field measurements before fabrication. Record measurements on shop drawings.  Coordinate field measurements and fabrication schedule with construction progress to avoid construction delays.

Install units in accordance with manufacturer’s safety and weather requirements.

Specifier Note:  Coordinate Article below with Conditions of the Contract and with Division 01 Closeout Submittals (Warranty) Section.  Use this Article to require special or extended warranty or bond covering the Work of this Section.

WARRANTY

Project Warranty:  Refer to Conditions of the Contract for project Warranty provisions.

Specifier Note:  Coordinate article below with manufacturer’s warranty requirements.  Visit the Andersen website for a complete description of the standard limited warranty including exclusions and limitations.

Manufacturer’s Warranty:  Submit, for Owner’s acceptance, manufacturer’s standard limited warranty document.  Manufacturer’s limited warranty is in addition to, and not a limitation of, other rights Owner may have under contract documents.

PRODUCTS

Specifier Note:  Retain article below for proprietary method specification.  Add product attributes, performance characteristics, material standards, and descriptions as applicable.  Use of such phrases as “or equal” or “or approved equal” or similar phrases may cause ambiguity in specifications.  Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

manufacturer

Provide products from the following manufacturer:

Andersen Windows, Inc.

100 4th Ave. N.

Bayport, MN  55003-1096.

Phone:  (800) 299-9029.

Fax:  (800) 752-9230.

E-mail:  technicalsupport@andersenwindows.com.

www.andersenwindows.com.

Local Contact:  <Specify contact information provided by local Andersen representative.>

manufactured units

Proprietary Products/Systems:  Wood windows, including the following:

Andersen® Architectural Specialty Windows.

Specifier Note:  Edit Article below to suit project requirements.  If substitutions are permitted, edit text below.  Add text to refer to Division 01 Project Requirements (Product Substitutions Procedures) Section.

Substitutions:  No substitutions permitted.

Specifier Note:  Specify materials to be furnished.  This article may be omitted and the materials can be included with the description of a manufactured unit, equipment, component, or accessory.

MATERIALS

Frame Members:  Fabricated from wood species approved in 101/I.S.2/NAFS.

Frame Cover:  Extruded aluminum with painted finish conforming to AAMA 2605.

specifier note:  retain project required color below.  delete colors not required.

Color:  White.

Color:  Sandtone.

Color:  Terratone®.

Color:  Forest Green.

GLAZING

General:  Provide dual sealed units consisting of high quality silicone foam spacer with hot butyl secondary seal.

Specifier Note: Select between the following standard glazing options. Consult Andersen Corporation for additional glazing options. In addition to complying with safety glazing requirements, tempered glass may be required because of window size and wind load. Consult Andersen Corporation for assistance in selecting appropriate glazing type.

Dual-Pane Insulating Glass Units:

Glass: Insulating glass units consisting of 2 lites of Clear annealed glass conforming to ASTM C1036, Type 1, Class 1, q3.

specifier note:  retain subparagraph above for non-tempered insulating glass units.  select subparagraph below for tempered insulating glass units.

Glass: Insulating glass units consisting of 2 lites of Clear tempered glass conforming to ASTM C1048, Type 1, Class 1, q3, Kind FT where indicated on Drawings and as required by window manufacturer.

Filling: Fill space between glass lites with air.

High-Performance™ Low-E Glass, Argon gas blend Filled Insulating Glass Units:

Glass:  Insulating glass units consisting of an outboard lite of clear annealed glass conforming to ASTM C1036, Type 1, Class 1, q3 and an inboard lite of clear annealed glass conforming to ASTM C1036, Type 1, Class 1, q3.

specifier note:  retain subparagraph above for non-tempered insulating glass units.  select subparagraph below for tempered insulating glass units.

Glass:  Tempered insulating glass units consisting of an outboard and inboard lite of clear tempered glass conforming to ASTM C1048, Type 1, Class 1, q3, Kind FT.

High-Performance™ Low-E Coating:  Magnetron sputtering vapor deposition (MSVD) Low-E coating applied to No. 2 surface.

Filling:  Fill space between glass lites with argon gas blend.

High-Performance Sun™ Low-E4™ Glass, Argon Gas Blend Filled Insulating Glass Units:

Glass: Insulating glass units consisting of 2 lites of Clear annealed glass conforming to ASTM C1036, Type 1, Class 1, q3.

specifier note:  retain subparagraph above for non-tempered insulating glass units.  select subparagraph below for tempered insulating glass units.

Glass: Insulating glass units consisting of 2 lites of Clear tempered glass conforming to ASTM C1048, Type 1, Class 1, q3, Kind FT where indicated on Drawings and as required by window manufacturer.

Magnetron sputtering vapor deposition (MSVD) TiO2 coating applied to the No. 1 surface.

High-Performance™ Low-E4™ Coating: Magnetron sputtering vapor deposition (MSVD) Low-E coating applied to the No. 2 surface.

Filling:  Fill space between glass lites with argon gas blend.

Protective removable polyolefin film applied to glass surfaces No. 1 and No. 4.

High-Performance  Low-E4™ Sun Glass, Low SHGC Argon Gas Blend Filled Insulating Glass Units:

Glass: Insulating glass units consisting of 2 lites of Clear annealed glass conforming to ASTM C1036, Type 1, Class 1, q3.

specifier note:  retain subparagraph above for non-tempered insulating glass units.  select subparagraph below for tempered insulating glass units.

Glass: Insulating glass units consisting of 2 lites of Clear tempered glass conforming to ASTM C1048, Type 1, Class 1, q3, Kind FT where indicated on Drawings and as required by window manufacturer.

Magnetron sputtering vapor deposition (MSVD) TiO2 coating applied to the No. 1 surface.

High-Performance™ Low-E4™ Sun Coating: Magnetron sputtering vapor deposition (MSVD) Low-E Sun coating applied to the No. 2 surface.

Filling:  Fill space between glass lites with argon gas blend.

Protective removable polyolefin film applied to glass surfaces No. 1 and No. 4.

ACCESSORIES

Specifier Note:  Consult specifications for grille material of adjacent unit for joined units of different types.  Consult Andersen Corporation for additional grille options.

Interior Grilles (False Muntin): Provide the following type of removable divided light grilles where indicated on Drawings.  Install removable grilles against interior glass with slide pins.  Provide dual face profile for muntin bar appearance from interior and exterior.

Specifier Note:  RETAIN PROJECT required material SUBPARAGRAPH BELOW AND DELETE SUBPARAGRAPHS NOT required.

Material:  Maple.

Material:  Pine.

Material:  Oak.

Material:  Mahogany.

Material:  Cherry.

Specifier Note:  RETAIN PROJECT required GRILLE style SUBPARAGRAPH BELOW AND DELETE SUBPARAGRAPHS NOT required.

Grille Style:  Colonial.

Grille Style:  Renaissance.

Grille Style:  Sunburst.

Grille Style:  Prairie A.

Grille Style:  Custom.

Specifier Note:  RETAIN PROJECT required GRILLE width SUBPARAGRAPH BELOW AND DELETE SUBPARAGRAPHS NOT required.

Grille Width:  3/4 inch (19.1 mm) wide.

Grille Width:  7/8 inch (22.2 mm) wide.

Grille Width:  1-1/8 inches (29 mm) wide.

Grille Width:  2-1/4 inches (57 mm) wide.

Specifier Note:  RETAIN PROJECT required exterior facing SUBPARAGRAPH BELOW AND DELETE SUBPARAGRAPHS NOT required.

Exterior Facing:  White color painted finish.

Exterior Facing:  Sandtone color painted finish.

Exterior Facing:  Terratone® color painted finish.

Exterior Facing:  Forest Green color painted finish.

Specifier Note:  RETAIN PROJECT required interior facing SUBPARAGRAPH BELOW AND DELETE SUBPARAGRAPHS NOT required.

Interior Facing:  Unfinished Maple.

Interior Facing:  Unfinished Pine.

Interior Facing:  Unfinished Oak.

Interior Facing:  Unfinished Mahogany.

Interior Facing:  Unfinished Cherry.

Interior Facing:  White painted finish.

Exterior Grilles:  Provide Fibrex® material high-profile or rigid vinyl low-profile exterior grilles where indicated on Drawings.  Permanently apply grilles to glass with adhesive tape.

Grille Color:  Match unit exterior color.

specifier note:  retain project required grille width subparagraph below.  delete subparagraphs not required.

Grille Width:  3/4 inch (19.1 mm).

Grille Width:  7/8 inch (22 mm).

Grille Width:  1-1/8 inch (29 mm).

Grille Width:  2-1/4 inch (57 mm).

Simulated Full Divided Light:  Provide 5/8 inch (16 mm) wide anodized aluminum spacer permanently mounted within insulating glass unit.  Align spacer to grille pattern to simulate full divided light appearance.

Specifier Note:  retain paragraph above for 5/8 inch spacer.  retain paragraph below for 7/8 inch spacer.

Simulated Full Divided Light:  Provide 7/8 inch (18 mm) wide anodized aluminum spacer permanently mounted within insulating glass unit.  Align spacer to grille pattern to simulate full divided light appearance.

Specifier Note:  For Finelight™ grilles, add the following.

Provide contour profile aluminum muntin bars permanently mounted within insulated glass unit where indicated on Drawings.

Grille Intersections:  ABS concealed plastic connectors with nylon end keepers.

Width:  3/4 inch (19.1 mm).

specifier note:  retain required width above or below.

Width:  1 inch (25.4 mm).

Color:  Match unit exterior color.

Specifier Note:  The following casing profiles listed below are consistent with Wood Moulding and Millwork Producers Association (WMMPA) WM Softwood Mouldings Pattern Catalog.  Consult an Andersen representative for additional casing styles.

Interior Casing:  Provide casing in the following material and style.  Provide straight pieces made from solid or veneered finger joined material.  Mill radial pieces from milled laminated wood.

specifier note:  retain project required wood type below.  delete wood types not required.

Casing Material:  Oak.

Casing Material:  Maple.

Casing Material:  Pine.

Casing Material:  Mahogany.

Casing Material:  Cherry.

specifier note:  retain project required profile below.  delete profiles not required.

Profile:  2-1/4 inches (57 mm) Colonial Style WM 366.

Profile:  2-1/2 inches (64 mm) Colonial Style WM351.

Profile:  3-1/2 inches (89 mm) Colonial Style WM444.

Profile:  2-1/4 inches (57 mm) Ranch WM324.

Profile:  2-1/2 inches (64 mm) Ranch WM315.

Extension Jambs:  Wood members machined from clear or veneered finger joined material, approved in 101/I.S.2/NAFS.

Vinyl Accessory Groove Filler:  Provide groove filler in the following color:

specifier note:  retain project required color below.  delete colors not required.

Color:  White.

Color:  Sandtone.

Color:  Terratone®.

Color:  Forest Green.

Specifier Note: Describe items that must be shop manufactured, fabricated or assembled before being delivered to site.

FABRICATION

Preservative Treatment:  Treat wood frame members and interior glazing stops after machining with water repellent preservative per WDMA I.S.4.

Frame Components:  Attach aluminum cover to wood frame.

Corner Fastening:  Fasten aluminum frame corners together using flat head screws and silicone sealant.

EXECUTION

MANUFACTURER’S INSTRUCTIONS

Comply with instructions and recommendations of window manufacturer.

Specifier Note:  Specify actions to physically determine that conditions are acceptable to receive primary products of Specification Section.

EXAMINATION

Site Verification of Conditions:  Verify that site conditions are acceptable for installation of units, including the following:

Concrete surfaces are dry and free of excess mortar, rocks, sand, and other construction debris.

Masonry openings are square and dimensions are correct.

Specifier Note:  Retain subparagraph below for wood framing.  Retain subparagraph above for masonry construction.

Rough openings are square and dimensions are correct.

Sill plates are level.

specifier note:  delete the following subparagraph is no wood framing on project.

Wood frame walls are dry, clean, sound, and well nailed or glued, free of voids and without offsets at joints.

Nail heads are driven flush with surfaces in openings and within 3 inches (75 mm) of rough opening.

Do not proceed with installation of units until unacceptable conditions are corrected.

Specifier Note:  Coordinate Article below with manufacturer’s recommended installation requirements.

INSTALLATION

General:

Remove unit components, parts, accessories, and installation guides from carton.

Inspect unit components and verify that components are not damaged and that parts are included before disposing of carton.

Shop-assemble multiple units before installation in accordance with manufacturer’s installation guides.

specifier note:  retain subparagraph above for shop-assembled units.  retain subparagraph below for field-assembled units.

Field-assemble multiple units before installation in accordance with manufacturer’s installation guides.

Interface with Other Work:

Perform installation in accordance with Manufacturer’s instructions.

Install units level, plumb, square, true to line, without distortion, anchored securely in place to structural support, and in proper relation to wall flashing and other adjacent construction.

Separate aluminum and other corrodible surfaces from sources of corrosion or electrolytic action at points of contact with other materials.

Install insulation in shim space around unit perimeter to maintain continuity of building insulation.  Do not overfill.

Hold back exterior siding or other finish materials from edge of unit to allow for expansion and contraction and installation of proper joint sealant with backing materials.  Seal perimeter of unit after exterior finish is applied per requirements of Division 07 “Joint Sealants” Section.

Finish interior units per requirements specified in related sections.  Refer to, and comply with, additional requirements in manufacturer’s installation guides.

Install optional hardware and unit accessories after cleaning.

Site Tolerances:

Adjust operation, insect screens, hardware, and accessories for a tight fit at contact points and weatherstripping for smooth operation and weathertight closure.

Specifier Note:  Specify final actions required to clean installed equipment or other completed Work to properly function or perform.  Coordinate Article below with Division 01 Execution Requirements (Cleaning) Section and specific Project requirements.

CLEANING

Clean units using cleaning material and methods specifically recommended by window manufacturer.

Remove excess sealants, glazing materials, dirt, and other substances.

Avoid damaging protective coatings and finishes.

Protect unit surfaces from masonry cleaning solution that could damage insulation glass panels or hardware.

Remove debris from work site and properly dispose of debris.

Specifier Note: Specify provisions for protecting work after installation but prior to acceptance by the owner. Coordinate article below with Division 01 Execution Requirements Section.

PROTECTION

Protect installed work from damage due to subsequent construction activity on the site.

END OF SECTION